ABSTRAK

STUDI FAULT ENHANCEMENT FILTER UNTUK INTERPRETASI STRUKTUR PADA DAERAH STRIKE-SLIP FAULT,

LAPANGAN “TIOMORA” TOP FORMASI DURI

CEKUNGAN SUMATERA TENGAH

Romario Paskah Tiomora Rajagukguk

NIM 115.100.009

Lapangan “TIOMORA” merupakan lapangan penghasil minyak dan gas bumi yang dioperasikan oleh PT. Chevron Pacific Indonesia yang berada pada jalur strike-slip fault. Keberadaan struktur pada lapangan ini mempengaruhi jebakan (trap) sehingga perlu dilakukan penelitian bawah permukaan dengan memanfaatkan data seismik. Fault enhancement filter adalah salah satu cara yang diharapkan mampu memberikan tampilan struktur secara tajam dan tidak ada noise. Untuk mendapatkan pola struktur bawah permukaan, digunakan juga atribut koherensi.

Koherensi adalah bagian dalam seismik atribut untuk membaca struktur yang tidak terlihat pada data seismik biasa berdasarkan perbedaan trace seismik di sekitar zona patahan, dan biasanya ditampilkan ke dalam satuan warna monochrome (hitam putih). Sedangkan fault enhancement filter adalah salah satu cara untuk meningkatkan kualitas data seismik dengan menggunakan dua teknik filter, yaitu median filter untuk menghilangkan noise dan diffusion filter untuk mendapatkan gambaran struktur yang lebih tajam pada penampang (section) seismik.

Berdasarkan pembacaan koherensi didapatkan pola struktur yang semula tidak dapat terbaca pada data seismik biasa, dan melalui hasil yang diperoleh dari pengolahan fault enhancement filter adalah adanya sesar-sesar baru pada time structure map yang berhasil terinterpretasikan jika dibandingkan dengan depth structure map yang sebelumnya tidak menggunakan pengolahan fault enhancement filter, khususnya pada bagian utara dan selatan peta.

Kata kunci: seismik atribut, koherensi, fault enhancement filter, strike-slip fault.

ABSTRACT

FAULT ENHANCEMENT FILTER STUDY FOR  STRUCTURAL INTERPRETATION OF STRIKE-SLIP FAULT AREA, “TIOMORA” FIELD

TOP DURI FORMATION, CENTRAL SUMATERA BASIN

Romario Paskah Tiomora Rajagukguk

NIM 115.100.009

“TIOMORA” field is an oil and gas field operated by PT. Chevron Pacific Indonesia has an effect by strike-slip fault. The fault in this area give an effect to make a trap for oil or gas so it’s necessary  to study the subsurface using seismic data. Fault enhancement filter is a methode that are expected to give the appearance of a sharp structure and no noise. To get the pattern of subsurface structures, used also attribute coherence.

Coherency is a part of seismic attribute to recite the structure wich doesn’t recite in normal seismic data based on the different of seismic traces in fault zone. Fault enhancement filter is a method to enhance seismic data quality use two filters technical, there are median filter to remove noise and diffusion filter to get a sharp figure of structure in seismic section.

Based on coherence recite, there are some structure model has interpretated wich doesn’t recite in normal seismic data, and from result of  fault enhancement there are some new faults in time structure map that not equivalent with depth structure map who not used fault enhancement filter technique, especially in north and south of map.

Keywords : Seismic attribute, coherency, fault enhancement filter, strike-slip

fault.